## Slide 1: Method of Hyperparameter Optimization of a Genetic Algorithm applied in Critical Scenario Generation for Autonomous Vehicles Master‘s Thesis Presentation

## Slide 2: Introduction
Testing the functionality of autonomous driving systems is crucial to ensure road safety
  Critical traffic scenarios are generated to validate these systems
Implementation:
  Autonomous driving functionality is applied on the EGO vehicle
  The Cumulated Emergency Brake Duration is the chosen criticality measure of a traffic scenario
  Genetic Algorithm optimizes the Cumulated Emergency Brake Duration of the EGO vehicle
    controls all other vehicles (NPCs) in the simulation

## Slide 3: Research Questions
Q1: Is a genetic algorithm suitable for generating critical driving scenarios compared to random search?
Q2: Can the performance of a genetic algorithm be improved by optimizing the control parameter using the Taguchi method?

## Slide 4: Simulation Setup
Traffic Manger provides a traffic simulation
  Vehicles and pedestrians move through the simulation in a realistic manner
  Provides an interface to alter individual actor behaviour through actions
    Example actions: LaneChange, JunctionSelection, ModifyTargetVelocity, CrossRoad, etc …
Genetic Algorithm optimizes the fitness function by directing NPCs through actions
Traffic Manger
Action Interface
NPC 1
Genetic Algorithm
Cost
NPC 2
NPC 3
…

## Slide 5: Genetic Algorithm Overview
Search algorithm inspired by the process of natural selection
  Can efficiently navigate large search spaces
Population-Based Optimization:
  Operates on a population of potential solutions (i.e., individuals)
  Solutions evolve over multiple generations
  Fitness function guides the selection of better individuals
  Utilizes crossover and mutation as genetic operators for reproduction
Chromosome:
  Consist of a list of genes and form a solution to the search problem
  Custom encodings are required
    Two different encodings were designed and compared
    Both encodings contain the actions for all NPCs for a whole simulation

## Slide 6: Hyperparameter Tuning
Literature review
  Recommended hyperparameter combinations gathered from existing literature
  32 different hyperparameter combinations tested over 5 repetitions
Taguchi Method
  Required 16 experiment runs over 8 repetitions
  Optimized:
    Three 4-level factors
    Four 2-level factors
    One interaction

## Slide 7: Hyperparameter Tuning – Taguchi Method
Developed by Genichi Taguchi for robust optimization
Part of Design of Experiment
  Systematic approach for process optimization
  Identifies factors (i.e., hyperparameters) impacting performance using ANOVA
  Identifies optimal factor-level (i.e., setting for each hyperparameter) combination
Advantages of Taguchi Method:
  Robustness, Cost-Efficiency, Simplicity
Orthogonal Arrays:
  Each factor is varied at different levels across different experimental trials
  Ensures that the effects of each factor and their interactions are isolated
Notes: While there are some other aspects to the Taguchi Method, I mainly focused on orthogonal arrays

## Slide 8: Genetic Algorithms Comparison
Settings | Literature Review | Taguchi Method
Number of Generations | 30 | 30
Population Size | 96 | 96
Crossover Type | Two Point | Uniform 0.5
Crossover Rate | 0.8 | 0.9
Mutation Rate | 0.2 | 0.3
Tournament Size | 4 | 4
Hyperparameter Combinations

## Slide 9: Evaluation
Comparison between:
  Optimized Genetic Algorithm – uses the resulting values from the Taguchi method
  Default Genetic Algorithm – uses best values from the literature review
  Random Search
Each algorithm was tested on
  4 different start scenarios
  10 repetitions per start scenario
Statistical Tools used:
  T-test
  Effect size

## Slide 10: Evaluation: Start Scenario 1

## Slide 11: Evaluation: Start Scenario 1

## Slide 12: Evaluation: Start Scenario 2

## Slide 13: Evaluation: Start Scenario 2

## Slide 14: Critical Situation 1
After pedestrian crossing
NPC vehicle cuts shortly before junction and violates path of EGO vehicle
EGO vehicle has to emergency break

## Slide 15: Critical Situation 2
Inside junction
NPC vehicle ignores right of way
EGO vehicle has to emergency break

## Slide 16: Critical Scenario 3
Kid runs over road
Kid is occluded by Truck
EGO vehicle (blue) has to emergency break

## Slide 17
Thank You!