## Slide 1: Method of Hyperparameter Optimization of a Genetic Algorithm applied in Critical Scenario Generation for Autonomous Vehicles Master‘s Thesis Presentation

## Slide 2: Introduction
Method for critical traffic scenario generation
  Can be used to validate safety of autonomous driving systems
Implementation:
  Autonomous driving functionality is applied on the EGO vehicle
  Genetic Algorithm optimizes the criticality of the traffic scenario
    Controls all other vehicles and pedestrians (NPCs) in the simulation
  The Cumulated Emergency Brake Duration of the EGO vehicle serves as the criticality measure

## Slide 3: Research Questions
Q1: Is a genetic algorithm suitable for generating critical driving scenarios compared to random search?
Q2: Can the performance of a genetic algorithm be improved by optimizing the control parameter using the Taguchi method?

## Slide 4: Simulation Setup
Traffic Manger provides a traffic simulation
  Vehicles and pedestrians move through the simulation in a realistic manner
  Provides an interface to alter individual actor behaviour through actions
    Example actions: LaneChange, JunctionSelection, ModifyTargetVelocity, CrossRoad, etc …
Genetic Algorithm optimizes the fitness function by directing NPCs through actions
Traffic Manger
Action Interface
NPC 1
Genetic Algorithm
Fitness
NPC 2
NPC 3
…

## Slide 5: Genetic Algorithm Overview
Search algorithm inspired by the process of natural selection
  Can efficiently navigate large search spaces
Population-Based Optimization:
  Operates on a population of individuals
  Individuals evolve over multiple generations
  Fitness function guides the selection of better individuals
  Best individuals reproduce using crossover and mutation operations
One individual consist of one chromosome
  One chromosome consists of a list of genes
  One chromosome describes one solution to the search problem
  Usually needs a custom encoding
    Two different encoding were designed to contain the actions for all NPCs for a whole simulation

## Slide 6: Genetic Algorithm – Chromosome Action Sequence
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
ModifyTargetVelocity(160%)
ModifyTargetVelocity(10%)
LaneChange(left)
LaneChange(right)
noAction()
Notes: Only one npc.
One gene represent one action.
The gene order corresponds the time steps of when the action is set.
No action is taken, so npc should continue on current trajectory

## Slide 7: Genetic Algorithm - Crossover Comparison
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
Two Point Crossover
+ Keeps sequences mostly intact
- Might struggle to maintain diversity
Notes: The fitness function will select 2 good performing individuals to reproduce using a crossover operation.
The resulting offspring will the move on into the next generation
Often not enough change introduced….

## Slide 8: Genetic Algorithm - Crossover Comparison
0
3
4
6
7
11
13
14
15
17
1
2
5
8
9
10
12
16
18
19
0
3
4
6
7
11
13
14
15
17
1
2
5
8
9
10
12
16
18
19
50% Uniform Crossover
+ Keeps diversity high
- Disruptive to sequences

## Slide 9: Hyperparameter Tuning
Literature review
  Recommended hyperparameter combinations gathered from existing literature
  32 different hyperparameter combinations tested over 5 repetitions
Taguchi Method
  Developed by Genichi Taguchi for robust optimization
  Part of Design of Experiment
    Systematic approach for process optimization
    Identifies factors (i.e., hyperparameters) impacting performance
    Identifies optimal factor-level (i.e., setting for each hyperparameter) combination
  Advantages of Taguchi Method:
    Provides a simple procedure for minimizing the number of experiment runs

## Slide 10: Hyperparameter Tuning – Taguchi Method
Required 16 experiment runs, to optimize
  Three 4-level factors
  Four 2-level factors
  and investigate one interaction between two factors
Each run was repeated 8 times
Results showed that the most significant hyperparameters are
  Selection Method
  Crossover Type
  Mutation Probability
Notes: Three hyperparameters, each having 4 possible settings

## Slide 11: Genetic Algorithms Comparison
Settings | Literature Review | Taguchi Method
Number of Generations | 30 | 30
Population Size | 96 | 96
Crossover Type | Two Point | Uniform 50%
Crossover Probability | 80% | 90%
Mutation Probability | 20% | 30%
Hyperparameter Combinations

## Slide 12: Evaluation
Comparison between:
  Optimized Genetic Algorithm – uses the resulting settings from the Taguchi method
  Default Genetic Algorithm – uses best settings from the literature review
  Random Search
Each algorithm was tested on
  4 different start scenarios
  Each experiment repeated 10 times

## Slide 13: Evaluation: Start Scenario Map
19 Vehicles
10 Pedestrians

## Slide 14: Evaluation: Results
Notes: Better text, better graphs

## Slide 15: Evaluation: Genetic Algorithm Comparison
Notes: Stops being able to increase his fitness value
Converges
Continue increasing its performance
Diversity quickly drops for default alg, which means that default is not able to have enough information in the population to continue expoliriing the search space
Can be contributed to the high disruptiveness of the optimized settings, which, while it was probably very disruptive to action sequences, meant that it is much more robust at avoiding local minimas.

## Slide 16: Critical Situation 1
Critical Situation after pedestrian crossing
NPC vehicle violates path of EGO vehicle
EGO vehicle has to emergency break

## Slide 17: Critical Situation 2
Critical Situation inside junction
NPC vehicle ignores right of way
EGO vehicle has to emergency break

## Slide 18: Critical Situation 3
Kid is occluded by Truck and runs over road
EGO vehicle has to emergency break

## Slide 19
Thank You!

## Slide 20: Evaluation: Start Scenario 2

## Slide 21: Evaluation: Start Scenario 2