## Slide 2: Introduction
Testing the functionality of Advanced Driver Assistance Systems or full stack autonomous vehicles is crucial to ensure road safety
Generate critical traffic scenarios using search-based testing
  A genetic algorithm will be used for the search task
    Controls all NPCs in the simulation
    Optimizes the cumulated emergency brake duration of the ego vehicle
Research Question 2
Can the performance of a genetic algorithm be improved by optimizing the control parameter using the Taguchi method?
Research Question 1
Is a genetic algorithm suitable for generating critical driving scenarios compared to random search?

## Slide 3: Traffic Manager – TODO: Maybe remove BT…
Traffic Manger
Action Interface
NPC 1
NPC 2
…
EGO
Behaviour Tree
Genetic Algorithm
World Information
World Information
Traffic Manger simulates all vehicle
  vehicles drive in then simulation in a realistic manner
  Provides an interface to alter vehicles behaviour through actions such as LaneChange, JunctionSelection, ModifyTargetVelocity, etc …
Genetic Algorithm optimizes the cost function by directing NPC vehicles through specified actions.
Behaviour Tree guides EGO vehicle by setting actions
  Sets different junction selections and avoiding blocking obstacles through lane changes in order to create more interesting scenarios

## Slide 4: Genetic Algorithm Implementation
Inspired by Natural Selection:
  Modeled after the process of natural selection in biology.
  Mimics the principles of evolution to find optimal solutions.
Population-Based Optimization:
  Operates on a population of potential solutions.
  Utilizes genetic operators like crossover and mutation for reproduction.
Iterative Improvement:
  Solutions evolve over multiple generations.
  Fitness function guides the selection of better solutions, leading to convergence.
Gene and Chromosome:
  A chromosome and its genes form a solution to the search problem
  Custom encodings for Genes and Chromosomes are required to describe a search solution

## Slide 5: Chromosome encodings
Corresponds to timestep 1 (0.5 seconds)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
Action NPC 1
Action NPC 2
…
Action NPC n
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
NPC 1
NPC 2
NPC 3
Corresponds to timestep 1 (0.5 seconds)
Action NPC 1
Time Encoding
Time+NPC Encoding

## Slide 6: Time Encoding – One Point Crossover
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19

## Slide 7: Time+NPC Encoding - One Point Crossover
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9

## Slide 8: Hyperparameter Tuning – Literature review
Literature review
  8 different hyperparameter combinations used by existing literature were tested over 5 repetitions
  Population size was varied over values 32, 48, 64 and 96
    A population size of 96 was the most robust
Design of Experiment:
  Systematic approach for process optimization.
  Identifies factors impacting performance.
  Introduction to Taguchi Method:
    Developed by Genichi Taguchi for robust optimization.
    Key Taguchi Concepts:
      Signal-to-Noise Ratio, Orthogonal Arrays, Control & Noise Factors.
    Advantages of Taguchi Method:
      Robustness, Cost-Efficiency, Simplicity.

## Slide 9: Taguchi Method – Step by Step
ANOVA
Main and Interaction Effects
Run experiment using modified L16 array
Linear Graph
L16 orthogonal array
Factor and Level Selection

## Slide 10: Comparison of Default vs Optimized Settings
Settings | Default | Optimized
PopulationSize | 96 | 96
CrossoverType | Two Point | Uniform 0.5
CrossoverRate | 0.8 | 0.9
MutationRate | 0.2 | 0.3
ChromosomeType | Time | Time+NPC
GeneType | Integer | Integer
TournamentSize | 4 | 4
IndMutationRate | 0.1 | 0.1

## Slide 11: Evaluation
Comparison between:
  Optimized Genetic Algorithm
  Default Genetic Algorithm – uses best values from the literature review
  Random Search
For each algorithm
  4 different start scenarios
  10 repetitions per start scenario
  2976 simulations per repetition
Goals
  Test if Optimized is than random (research question 1)
  Test if Optimized is better than default (research question 2)
  Analyse if Optimized can generalize on different start scenarios where it has not been optimized on

## Slide 12: Evaluation: Start Scenario 2

## Slide 13: Evaluation: Start Scenario 2

## Slide 14: Evaluation: Start Scenario 4

## Slide 15: Evaluation: Start Scenario 4

## Slide 16: Evaluation: Start Scenario 3

## Slide 17: Evaluation: Start Scenario 3

## Slide 18: Critical Situation 1 – Scenario 1 - Carla
After pedestrian crossing
NPC vehicle cuts shortly before junction and violates path of EGO vehicle (blue)
EGO vehicle must perform an emergency break

## Slide 19: Example videos – rendered in Carla
Inside junction
NPC vehicle ignores right of way
EGO vehicle (blue) must perform emergency break to avoid crash

## Slide 20: Example videos – rendered in Carla
Kid runs over road
Kid is occluded by Truck
EGO vehicle (blue) has to emergency break

## Slide 22: Gene Encoding
0 = NoAction
1 = JunctionSelection(straight)
2 = JunctionSelection(left)
3 = JunctionSelection(right)
4 = LaneChange(left, 3)
5 = LaneChange(right, 3)
6 = AbortLaneChange()
7 …
{"type": "LaneChange", "direction": "left", "duration": 3}
{"type": "JunctionSelection", "junction_selection_angle": "straight"}
{"type": “AbortLaneChange"}
{"type": “ModifyTargetVelocity“, “percentage“: “133.4”}
Encode as dictionary
Encode as Integer

## Slide 23: Behavior Tree

## Slide 25: Evaluation: Start Scenario 1

## Slide 26: Evaluation: Start Scenario 1

## Slide 27
ADD: pop size results
Add: all actions